## Slide 1: Bridging Hydrology and Thermodynamics with an Interface Model of Freeze-Thaw
Élise Devoie, James R. Craig
Civil & Environmental Engineering, University of Waterloo, Waterloo, ON
Notes: For applications in the changing cold regions of Canada

## Slide 2
Study Site
Notes: Discontinuous PF
3 landcover types

## Slide 3: Permafrost Thaw
1947 (70.4 ± 9 %
2008 (43.3 ± 8 %
Permafrost
Permafrost - Free
Lake
Quinton, W. L., Hayashi, M., & Chasmer, L. E. (2011)

## Slide 4: Hydrological Impacts of Ground Ice
Infiltration impedance
Moisture migration
Winter quiescence
Soil destabilization
Gray et al. 2001; Harlan 1973; Stähli et al. 1999; Woo 2012; Nelson et al. 2001
Notes: Permafrost or seasonal ground ice

## Slide 5: Existing Models of Ground Ice
Model Type | Pros | Cons | Example
Continuum | Non-equilibrium Multiple fonts | Numerically expensive Saturated (usually) Unstable | SUTRA-ICE Mcclymont et al.; (2013) McKenzie et al. (2007)
Front-tracking | Relatively efficient | Steady-forcing Single front Saturated | Stefan solution; Hayashi et al. (2007)

## Slide 6: Objective
Develop a
  Computationally efficient
  Semi-analytical
  Non-equilibrium
  Variably-saturated
  Multi-layered
  Stable
model to describe
  Seasonal frost
  Active layer
  Permafrost

## Slide 7: Outline
Model description
Benchmarking
  Stefan
  Mass Balance
  Unsaturated
Model Efficiency Comparison
Application
  Observed thaw rates

## Slide 8: Interface Model
Dynamic domain elements defined by soil properties
Interfaces move based on mass and energy transfer
Simple mass balance
Temperatures profile determined by superposition of analytic solutions

## Slide 9: The proof is in the numbers!
Freeze-thaw front
Water balance (equilibrium)
* Flux dependent on saturation and ice content

## Slide 10: The proof is in the numbers!
Free boundary problem – Saturated
Free boundary problem – Unsaturated
Confined layer – Saturated

## Slide 11: Outline
Model description
Benchmarking
  Stefan
  Saturated
  Unsaturated
Model Efficiency Comparison
Application
  Observed thaw rates

## Slide 12: Stefan Problem Benchmark
0.5 cm error, 100 days
1.0 cm error, 1000 days
Notes: Properties of water
IC : Uniform 0˚C
BC: Constant 5˚C

## Slide 13
Saturated Model Benchmark
Time [days]
Depth below ground [m]
Thawed
Frozen
Frozen
Slushy
Notes: FONT SIZE
Animate appearance of T in left
Flip xy left
Darkem T in left
Label zones in right plot

## Slide 14: Unsaturated Model Benchmark

## Slide 15: Unsaturated Model Benchmark

## Slide 16: Unsaturated Model Benchmark

## Slide 17: Outline
Model description
Benchmarking
  Stefan
  Mass Balance
  Unsaturated
Model Efficiency Comparison
Application
  Observed thaw rates

## Slide 18: Model Efficiency Comparison
Model Type | Finite Volume | Interface | Interface
Timestep | 1 h | 1 h | 24 h
Run time | 1275 s (21 min) | 63 s (1 min) | 4 s
5 year simulation
Unsaturated
Notes: % year simulaton
Note 24h stability difference

## Slide 19: Outline
Model description
Benchmarking
  Stefan
  Mass Balance
  Unsaturated
Model Efficiency Comparison
Application
  Observed thaw rates

## Slide 20: Application: Permafrost Degradation Rates
10 000 surface temperature series sampled from SARIMA models
  PERMAFROST
  TALIK
Initial talik thickness sampled from uniform distribution
Notes: Font size

## Slide 21: Temperature Boundary Conditions
TALIK
PERMAFROST
Time [years]
Temperature [C]
Notes: Font size

## Slide 22: Permafrost Degradation: Field Data
Talik
No
Talik
Change in
Depth to Permafrost [cm]
Connon et al. 2017
Modelled
Measured
Notes: This plot belings in the garbage

## Slide 23: Conclusion
Next Steps
  Test in other environments
  Seasonal frost
  Frost heave
  Incorporation into hydrologic models
23
The interface model presented is
  Fast!
  Variably-saturated
  Unconditionally Stable
Allowing for:
  Uncertainty analysis
  Sensitivity analysis
  Stochastic simulations
  Extended simulation duration

## Slide 24: Acknowledgements
Many thanks to those who contributed to fieldwork and advised model development: Caren Ackley, Erfan Amiri, Dr. Nandita Basu, Michael Braverman, Genevieve Brown, Dr. Ryan Connon, Dr. James Craig, Dirk Friesen, Gabriel Hould Gosselin, Sarah Grass, Dr. Julie Mai, Dr. Jonathan Price, Dr. William Quinton, Lindsay Stone, and others.

## Slide 25: Permafrost Degradation: Positive Feedback
Connon et al. 2017
Talik formation
Subsidence and ponding
Canopy degradation and
Increased conductivity
Advection
Increased radiation
Connon et al. 2018
Talik
No
Talik
Change in
Depth to Permafrost [cm]
Modelled
Measured

## Slide 26
Measurements with talik (supra-permafrost layer > 80 cm)
Connon et al. 2017
 | Transect | Grid
2011 | 20% | 8%
2015 | 48% | 33%
Permafrost disequilibrium
Connon et al. 2018

## Slide 27: Taliks
Isolated
Confined
Open
Connected
Confined
Wetland
Notes: Ground that is frozen for two or more consecutive years
Talik – confined, trhough, isolated, connected
Active Layer
Frost Table
Permafrost Table

## Slide 28: Taliks
Isolated
Confined
Connected
Confined
Wetland
Notes: Ground that is frozen for two or more consecutive years
Talik – confined, trhough, isolated, connected
Active Layer
Frost Table
Permafrost Table